## Slide 1: 2.4 GHz vs 868 MHz
II – Management and Performance Analysis Sensor Networks
Mats De Meyer & Quentin Van Ravels

## Slide 2: Introduction
2.4 GHz Wi-Fi, Bluetooth, 802.15.4 Much interference Less propagation | 868 MHz Less commonly used Less interference Better propagation  Good potential!

## Slide 3: Goal
Compare Latency, Throughput and Power Consumption of 2.4 GHz and 868 MHz bands

## Slide 4: Setup
Radios:
cc1200 for 868 MHz
cc2538 for 2.4 GHz
Contiki
nullrdc
CSMA
rime
  Receiver address 2d:c8
  Sender address 2d:f9

## Slide 5: Power Consumption
Method

## Slide 6: Power Consumption
C Program based on send-unicast.c
sends 300 messages
one message every second
10 second delay to avoid startup anomalies
payload: string of 5 characters
On the receiving node, receive-unicast.c

## Slide 7: Power Consumption
Two types of measurements:
Energest
KeySight N6705B DC Power Analyzer

## Slide 8: Energest
Contiki module for software-based energy estimation
Tracks time of different modes: CPU, LPM, IRQ, TRANSMIT, LISTEN
ticks converted to seconds (32768 ticks = 1 sec)
Convert logs with python script for readability and ease of use
calculate charge: multiply cumulative time value by current (Q = I * t)
calculate energy: multiply by Volt (E = Q * V)
Convert to mWh

## Slide 9: Energest

## Slide 10: KeySight DC Power Analyzer
Powers the motes at 3.7V
single run of 5 min and 30 seconds (x 10)
export to csv and clean with python script
But data is power, voltage and current per timestamp
 Get cumulative charge / energy for comparison

## Slide 11: Power Consumption
Results

## Slide 12: Energest

## Slide 13: Latency
Method

## Slide 14: Latency
Same logic, packet counter now sent as payload
 run 5 times for each radio
 print modified timestamp at sender and receiver
Python script
 use pandas package to calculate timestamp difference of 1500 packages
 plot confidence intervals

## Slide 15: Latency
Results

## Slide 16: Latency

## Slide 17: Packet Delivery Ratio
Method & Results

## Slide 18: PDR
Check latency results
 send and receive with address and packet number
 100% (1500/1500) on both frequencies

## Slide 19: Conclusion

## Slide 20: Conclusion
868 MHz higher latency due to lower data rate and frequency
PDR 100% because of high delay between packages (1 second) and acks
Power Consumption inconclusive, but same order of magnitude
Both feasible options, trade offs have to be made